SPECIFICATIONS FOR INSITE MULTI-CHANNEL

SUSPENDED SOLIDS MONITOR with SENSORS SUITABLE

FOR CLASS 1, DIVISION 2 AREAS

  - GENERAL REQUIREMENTS:

- The SS system shall be an INSITE Model MPA48 multi-channel channel Suspended Solids Analyzer with up to eight Suspended Solids Sensors and up to eight barrier junction boxes.  It shall consist of the analyzer, sensors with up to 200 feet of cable, barrier junction boxes, and mounting hardware. The sensors shall be a type that measures the amount of infrared energy absorbed across a fixed sensor gap.

  - PRODUCT SPECIFICATIONS:

Analyzer

- The monitor shall be housed in a fiberglass NEMA 4X enclosure with brackets for wall or standard round handrail mounting.

- It shall have a digital display controlled by microprocessor circuitry.

- All run, programming, and calibration functions shall be accessible without having to open the enclosure.

- Provide 4 relays discrete outputs.

- Continuously display suspended solids in mg/l for up to eight sensors.

- Provide an extended temperature, UV treated LCD digital display for continuously showing dissolved oxygen and temperature readout. Programming and diagnostics are also provided through this display.

- Provide self-diagnostics for the sensor and analyzer.  Analyzer shall have error messages in the operating mode for higher or lower than normal sensor output voltage, unstable instrument circuitry, unstable output of the sensor, and weak sensor output level.

- Provide isolated RS-485 MODBUS RTU serial communication port for suspended solids sensors and relay status.

- Provide 4-20 MADC optically isolated outputs for all suspended solids sensors.

- Provide standard back-lit LCD display.

- InsiteIG Model MPA48 analyzer

Sensors

- The sensors shall be a type that measures the amount of infrared energy absorbed across a fixed sensor gap. The sensor will automatically compensate for ambient light and not be affected by changes in process color.

- Ambient Temperature Range: -20ºC ≤ TAMB ≤ +50º C

- Suspended Solids Range: 0 to 30,000 mg/l

- Resolution: 3 significant digits, 1 mg/l minimum

- Drift: Typically less than 1% per year

- Suitable for outdoor use - submerged

Class 1 Division 2 Groups A, B ,C, D, T6 per

ANSI/ISA 12.12.01-2015 and CAN/CSA C22.2 No. 213-15

- Up to eight InsiteIG Model 14 sensors

Barrier Junction Boxes

- Ambient Temperature Range: -20ºC ≤ TAMB ≤ +50º C

- Normal operating input: 8.5Vdc at 50 mA.

- Voltages in excess of 9.5Vdc may blow a non-replaceable fuse

- Currents in excess of 100 mA may blow a non-replaceable fuse

- Suitable for outdoor use. NEMA 4x (IP66)

- Up to eight InsiteIG Model SJB-1 junction boxes