SPECIFICATIONS FOR INSITEIG SUSPENDED SOLIDS SENSOR

(MODEL M15-33)

The SS sensor shall be a type that will automatically compensate for ambient light and any process color changes. The sensor will use a 880 nanometer emitter. The sensor will automatically compensate for temperature variations.

The suspended solids sensor will have a five year warranty and will not require any consumable or spare parts during this period with normal field deployment. Sensor will come standard with a tool free ¼" O. D. tubing connector for implementing automatic self cleaning.

Specific suspended solids sensor requirements in addition to the above are:

- Measuring Range: 0 to 30,000 mg/l total suspended solids

- Accuracy: +/- 5% of the reading or +/- 100 mg/l whichever is greater

- Repeatability: +/- 1% of the reading or +/- 20 mg/l whichever is greater

- Response Time: 95% in under 60 seconds

- Resolution: 
1 mg/l below 1000 mg/l,
10 mg/l from 1001 to 9999 mg/l,
100 mg/l above 10,000 mg/l

- Drift: less than 1% per year

- Temp. Range: 0°C to 60°C

- 1-½" MNPT mounting thread

- 33ft (10m) sensor cable – custom lengths available

- ¼" O.D. tube connection for jet cleaning